## Slide 1: Open Weather and JSON Point Features
106th OGC Technical Committee
Orléans, France
Richard Carne, Mark Burgoyne
20 March 2018

## Slide 2: What is Open Weather
Open Weather initiative:
Create standards for common and consistent access to weather data for Developers without Met Ocean Domain experience.
Standard approach to accessing and describing global weather data from multiple providers.
Maintaining authoritative voice and attribution.

## Slide 3: Open Weather
Implementation
Data and access standards
Building supported system to enable multiple NHMS to provide weather data services to developers in common and consistent manner.
Defining the data formats and access patterns for a range of Met Ocean data as a community standard, enabling developers to easily access global data from multiple providers.
Two distinct activities:
OGC
WMO / Open WIS
Notes: Federated approach to building service. i.e. data is not centrally stored but a central interface layer (Inteligent GeoProxy) would direct spatial queries to the best API end point and return a common data object.

## Slide 4: Types of Users
Users are predominantly application developers with limited knowledge of Met and Ocean data types.
Also limited knowledge of / desire to work with WFS and WCS
Familiar with W3C and standards such as JSON.
Developing applications that are not primarily focused on Met and ocean data.

## Slide 5: Point Features
The type of GeoJSON object, the default for Open Weather will be FeatureCollection
Data format
The Open Weather format is based on GeoJSON but extends it to provide the extra metadata required to describe the information returned by the users query. The core parts of GeoJSON object are as follows:
Type
Features
An array of Feature objects which contain the data values.
bbox
A bounding box which defines an area which encompasses all of the features with the FeatureCollection.
Notes: The key point here is that although a data may be produced in a specific coordinate system, the location will always be described at the high level using WGS:84 (this will allow data consumers to easily identify if the information is in their area of interest). The idea being that the data's original coordinate system values can be included as a value in the properties section and described in the Metadata section.
Another essential is a consistent approach to describe the time that the information in the service last changed and the time periods that the data values are representative of.

## Slide 6: Point Features
Open Weather extends the format by adding two new values:
This defines when the data was created, links to Licensing details, links to the terms and conditions and any text that should be included for attributions.
metadata
An array of parameter objects, these follow the same specification as that defined for CoverageJSON https://github.com/covjson/specification/blob/master/spec.md
parameters
Notes: The Metadata section is fairly open to customization, but ideally where possible (to keep the payload as small as possible) the information should be provided as links to more detail.
Is this section needed, are there already ways to define data creation date?
Again the parameter section should only have the basic essential information (I.e. the units) included in the body of the message with more detail provided by linking to registries

## Slide 7: Example Metadata Object
"metadata": {
"date_created": "2017-12-01T10:00:00+0100",
"terms": "https://www.met.no/en/free-meteorological-data/Licensing-and-crediting",
"Start date": "2017-12-01T07:00:00+0100",
"Next model": "2017-12-01T10:00:00+0100",
"End date": "2017-12-03T18:00:00+0100",
"link": "https://www.met.no/en",
"model": "LOCAL",
"Model run ended": "2017-12-01T02:27:46+0100",
"credit": "Weather forecast from the Norwegian Meteorological Institute" }

## Slide 8: Example Parameter Object
{
"type" : "Parameter",
"description" : {"en": "The sea surface temperature in degrees Celsius."},
"observedProperty" : {
"id" : "http://vocab.nerc.ac.uk/standard_name/sea_surface_temperature/",
"label" : {"en": "Sea Surface Temperature"},
"description" : {"en": "The temperature of sea water near the surface (including the part under sea-ice, if any), and not the skin temperature."}
},
"unit" : {
"label" : {"en": "Degree Celsius"},
"symbol": { "value": "Cel", "type": "http://www.opengis.net/def/uom/UCUM/" }
}
}

## Slide 9: Data Types
Proposed list of Data Types that Must be supported by Open Weather compatible APIs:
Air Temperature - Temperature value for the defined time
Wind Speed - Wind speed for the defined time
Wind Direction - Wind direction in decimal degrees for the defined time
Weather Text - Short Text description of weather conditions for the defined time
Weather Icon - Link to an icon describing weather conditions for the defined time
Maximum Air Temperature - Maximum Temperature value for the defined time period
Minimum Air Temperature - Minimum Temperature value for the defined time period

## Slide 10: Required Query Options
Proposed list of required query types supported by the Point Feature API:
Position of request - Query parameter to define location to return data for either :
  Latitude and Longitude - in decimal degrees
Or (in order to simplify query caching):
  GeoHash - A GeoHash encoding of the latitude and longitude of the request
Units - Query parameter to define the type of units to return Metric or Imperial, by default Open Weather API's should return data in Metric units

## Slide 11: Next Steps
Feedback and comments – Now is your chance!
Assess overlaps with Pete Trevelyan’s work (API design for Met Ocean extraction)
Form a working group to progress Met Ocean API standards